## Slide 1: Multipath TCP
Olivier Bonaventure
http://inl.info.ucl.ac.be
Thanks to Sébastien Barré, Christoph Paasch, Grégory Detal, Mark Handley, Costin Raiciu, Alan Ford, Micchio Honda, Fabien Duchene and many others
November 2012

## Slide 2: Agenda
The motivations for Multipath TCP
The changing Internet
The Multipath TCP Protocol
Multipath TCP use cases

## Slide 3: The origins of TCP
Source : http://spectrum.ieee.org/computing/software/the-strange-birth-and-long-life-of-unix
Notes: Mention coverage, performance, range, etc.

## Slide 4: The Unix pipe model
echo
wc
1234 abbsbbbs

## Slide 5: The TCP bytestream model
Client
Server
ABCDEF...111232
0988989 ... XYZZ
IP:1.2.3.4
IP:4.5.6.7

## Slide 6: Endhosts have evolved
Mobile devices have multiple wireless interfaces

## Slide 7: User expectations

## Slide 8: What technology provides
3G celltower
IP 1.2.3.4
Notes: ajouter adresse ip

## Slide 9: What technology provides
3G celltower
IP 1.2.3.4
IP 5.6.7.8

## Slide 10: What technology provides
3G celltower
When IP addresses change TCP connections have to be re-established !
IP 1.2.3.4
IP 5.6.7.8

## Slide 11: Equal Cost Multipath
ECMP implementation
Packet arrival :
Hash(IPsrc, IPdst, Prot, Portsrc, Portdst) mod #oif
Packets from one TCP connection follow same path
Different connections follow different paths
Notes: connexion tp versus paquets

## Slide 12: How prevalent is ECMP ?
Analysis of ISP network topologies
G. Detal, Ch. Paasch, S. van der Linden, P. Mérindol, G. Avoine, O. Bonaventure, Revisiting Flow-Based Load Balancing: Stateless Path Selection in Data Center Networks, to appear in Computer Networks

## Slide 13: Datacenters
Notes: Mention coverage, performance, range, etc.

## Slide 14: ECMP in datacenters
G. Detal, Ch. Paasch, S. van der Linden, P. Mérindol, G. Avoine, O. Bonaventure, Revisiting Flow-Based Load Balancing: Stateless Path Selection in Data Center Networks, to appear in Computer Networks

## Slide 15: IPv4 and IPv6 paths are not always congruent
IP=3.4.5.6
IP6=2a00:1450:400c:c05::69
IP6=2a00:cafe::1
IP=3.4.5.6

## Slide 16: IPv4 and IPv6 performance may differ
E. Aben, Measuring World IPv6 Day - Comparing IPv4 and IPv6 Performance,
https://labs.ripe.net/Members/emileaben/measuring-world-ipv6-day-comparing-ipv4-and-ipv6-performance

## Slide 17: IPv4 versus IPv6 performance
E. Aben, Measuring World IPv6 Day - Comparing IPv4 and IPv6 Performance,
https://labs.ripe.net/Members/emileaben/measuring-world-ipv6-day-comparing-ipv4-and-ipv6-performance

## Slide 18: Agenda
The motivations for Multipath TCP
The changing Internet
The Multipath TCP Protocol
Multipath TCP use cases

## Slide 19: The Internet architecture that we explain to our students
Physical
Datalink
Network
Transport
Application
O. Bonaventure, Computer networking : Principles, Protocols and Practice, open ebook, http://inl.info.ucl.ac.be/cnp3
Physical
Physical
Datalink
Physical
Datalink
Network

## Slide 20: A typical "academic" network
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Physical
Datalink

## Slide 21: The end-to-end principle
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Physical
Datalink
TCP

## Slide 22: In reality
  almost as many middleboxes as routers
  various types of middleboxes are deployed
Sherry, Justine, et al. "Making middleboxes someone else's problem: Network processing as a cloud service." Proceedings of the ACM SIGCOMM 2012 conference. ACM, 2012.

## Slide 23: A middlebox zoo
http://www.cisco.com/web/about/ac50/ac47/2.html
Web Security Appliance
NAC Appliance
ACE XML Gateway
Streamer
VPN Concentrator
SSL Terminator
Cisco IOS Firewall
IP Telephony Router
PIX Firewall Right and Left
Voice Gateway
Content Engine
NAT

## Slide 24: How to model those middleboxes ?
In the official architecture, they do not exist
In reality...
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
TCP
Physical
Datalink
Network
Transport
Application

## Slide 25: TCP segments processed by a router
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 26: TCP segments processed by a NAT
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Notes: c

## Slide 27: TCP segments processed by a NAT (2)
active mode ftp behind a NAT
220 ProFTPD 1.3.3d Server (BELNET FTPD Server) [193.190.67.15]
ftp_login: user `<null>' pass `<null>' host `ftp.belnet.be'
Name (ftp.belnet.be:obo): anonymous
---> USER anonymous
331 Anonymous login ok, send your complete email address as your password
Password:
---> PASS XXXX
---> PORT 192,168,0,7,195,120
200 PORT command successful
---> LIST
150 Opening ASCII mode data connection for file list
lrw-r--r-- 1 ftp ftp 6 Jun 1 2011 pub -> mirror
226 Transfer complete

## Slide 28: TCP segments processed by an ALG running on a NAT
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options

## Slide 29: How transparent is the Internet ?
© O. Bonaventure, 2011
25th September 2010 to 30th April 2011
142 access networks
24 countries
Sent specific TCP segments from client to a server in Japan
Honda, Michio, et al. "Is it still possible to extend TCP?" Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 30: How to extend TCP ? RFC1323
Large window extension
  supports >64KBytes windows by shifting window field in TCP segment header
SYN+WScale=10
SYN+WScale=10
SYN+ACK
WScale=4
SYN+ACK
WScale=4
Snd.Wind.Scale=10
Rcv.Wind.Scale=?
Snd.Wind.Scale=4
Rcv.Wind.Scale=
4
10
Notes: peut-être supprimer la partie rfc1323

## Slide 31: How to extend TCP ? RFC1323
What happens with middleboxes ?
SYN+WScale=10
SYN
SYN+ACK
SYN+ACK
Snd.Wind.Scale=10
Rcv.Wind.Scale=?
Snd.Wind.Scale=
Rcv.Wind.Scale=
0
0
0
0

## Slide 32: How to extend TCP ? RFC1323
What happens with middleboxes ?
SYN+WScale=10
SYN+WScale=10
SYN+ACK
SYN+ACK
WScale=4
Snd.Wind.Scale=10
Rcv.Wind.Scale=?
Snd.Wind.Scale=
Rcv.Wind.Scale=
?
0
0
4
10

## Slide 33: End-to-end transparency today
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Middleboxes don't change
the Protocol field, but
many discard packets with an unknown Protocol field

## Slide 34: Agenda
The motivations for Multipath TCP
The changing Internet
The Multipath TCP Protocol
Multipath TCP use cases

## Slide 35: Design objectives
Multipath TCP is an evolution of TCP
Design objectives
  Support unmodified applications
  Work over today’s networks
  Work whenever TCP would work

## Slide 36: TCP Connection establishment
Three-way handshake
SYN,seq=1234,Options
SYN+ACK,ack=1235,seq=5678,Options
ACK,seq=1235,ack=5679

## Slide 37: Data transfer
seq=1234,"abcd"
ACK,ack=1238,win=4
seq=1238,"efgh"
ACK,ack=1242,win=0

## Slide 38: Connection release
seq=1234,"abcd"
RST

## Slide 39: Connection release
seq=1234,"abcd"
ACK,ack=1239
FIN,ack=350
seq=345,"ijkl"
FIN, seq=1238
FIN,seq=349

## Slide 40: Identification of a TCP connection
  Four tuple
  IPsource
  IPdest
  Portsource
  Portdest
  All TCP segments contain the four tuple
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 41: The new bytestream model
41
Client
Server
ABCDEF...111232
0988989 ... XYZZ
IP:1.2.3.4
IP:4.5.6.7
IP:2.3.4.5
IP:6.7.8.9
B
C
D
A
Notes: arrive fort tard

## Slide 42: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 43: A naïve Multipath TCP
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"
SYN+Option

## Slide 44: A naïve Multipath TCP In today's Internet ?
SYN+Option
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"
There is no corresponding TCP connection

## Slide 45: Design decision
  A Multipath TCP connection is composed of one of more regular TCP subflows that are combined
    Each host maintains state that glues the TCP subflows that compose a Multipath TCP connection together
    Each TCP subflow is sent over a single path and appears like a regular TCP connection along this path

## Slide 46: Multipath TCP and the architecture
Physical
Datalink
Network
Transport
Application
Multipath TCP
TCP1
socket
TCP2
TCPn
...
Application
A. Ford, C. Raiciu, M. Handley, S. Barre, and J. Iyengar, “Architectural guidelines for multipath TCP development", RFC6182 2011.

## Slide 47: A regular TCP connection
What is a regular TCP connection ?
  It starts with a three-way handshake
    SYN segments may contain special options
  All data segments are sent in sequence
    There is no gap in the sequence numbers
  It is terminated by using FIN or RST

## Slide 48: Multipath TCP
SYN+Option
SYN+ACK+Option
ACK
SYN+OtherOption
SYN+ACK+OtherOption
ACK

## Slide 49: How to combine two TCP subflows ?
SYN+Option
SYN+ACK+Option
ACK
SYN+OtherOption
SYN+ACK+OtherOption
ACK
How to link with
blue subflow ?

## Slide 50: How to link TCP subflows ?
SYN, Portsrc=1234,Portdst=80+Option
SYN+ACK[...]
ACK
SYN, Portsrc=1235,Portdst=80
+Option[link Portsrc=1234,Portdst=80]
A NAT could change addresses and port numbers

## Slide 51: How to link TCP subflows ?
SYN, Portsrc=1234,Portdst=80 +Option[Token=5678]
SYN+ACK+Option[Token=6543]
ACK
SYN, Portsrc=1235,Portdst=80
+Option[Token=6543]
MyToken=5678
YourToken=6543
MyToken=6543
YourToken=5678

## Slide 52: Subflow agility
Multipath TCP supports
  addition of subflows
  removal of subflows

## Slide 53: TCP subflows
Which subflows can be associated to a Multipath TCP connection ?
  At least one of the elements of the four-tuple needs to differ between two subflows
    Local IP address
    Remote IP address
    Local port
    Remote port

## Slide 54: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 55: How to transfer data ?
seq=123,"a"
seq=124,"b"
seq=125,"c"
seq=126,"d"
ack=124
ack=126
ack=125
ack=127

## Slide 56: How to transfer data in today's Internet ?
seq=123,"a"
seq=124,"b"
seq=125,"c"
ack=124
ack=126
ack=125
Gap in sequence numbering space
Some DPI will not allow this !

## Slide 57: Multipath TCP Data transfer
Two levels of sequence numbers
Multipath TCP
TCP1
socket
TCP2
Multipath TCP
TCP1
socket
TCP2
ABCDEF
Data sequence #
TCP1 sequence #
TCP2 sequence #

## Slide 58: Multipath TCP Data transfer
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=2, seq=124,"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457

## Slide 59: Multipath TCP How to deal with losses ?
Data losses over one TCP subflow
  Fast retransmit and timeout as in regular TCP
Dseq=0,seq=123,"a"
DAck=1,ack=124
Dseq=0,seq=123,"a"
DAck=1,ack=124

## Slide 60: Multipath TCP
What happens when a TCP subflow fails ?
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=0,ack=457
Dseq=0,seq=457,"a"
DAck=2,ack=458

## Slide 61: Retransmission heuristics
Heuristics used by current Linux implementation
  Fast retransmit is performed on the same subflow as the original transmission
  Upon timeout expiration, reevaluate whether the segment could be retransmitted over another subflow
  Upon loss of a subflow, all the unacknowledged data are retransmitted on other subflows

## Slide 62: Flow control
How should the window-based flow control be performed ?
  Independant windows on each TCP subflow
  A single window that is shared among all TCP subflows

## Slide 63: Independant windows
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=100
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=100
DAck=1,ack=124,win=0

## Slide 64: Independant windows possible problem
Impossible to retransmit, window is already full on green subflow
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=0

## Slide 65: A single window shared by all subflows
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=10
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=10
DAck=1,ack=124,win=10

## Slide 66: A single window shared by all subflows Impact of middleboxes
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=100
DAck=1,ack=124,win=100
DAck=2,ack=457,win=5

## Slide 67: Multipath TCP Windows
Multipath TCP maintains one window per Multipath TCP connection
  Window is relative to the last acked data (Data Ack)
  Window is shared among all subflows
    It's up to the implementation to decide how the window is shared
  Window is transmitted inside the window field of the regular TCP header
  If middleboxes change window field,
    use largest window received at MPTCP-level
    use received window over each subflow to cope with the flow control imposed by the middlebox

## Slide 68: Multipath TCP buffers
Multipath TCP
TCP1
socket
TCP2
Scheduler
Transmit queues, process only regular TCP header
Reorder queue, processes only TCP header
MPTCP-level, resequencing possible
send(...)
recv(...)

## Slide 69: Multipath TCP
How to exchange the Multipath TCP specific information between two hosts ?
Option 1
  Use TLVs to encode data and control information inside subflows
Option 2
  Use TCP options to encode all Multipath TCP information

## Slide 70: Multipath TCP with only options
Advantages
  Normal way of extending TCP
  Should be able to go through middleboxes or fallback
Drawbacks
  limited size of the TCP options, notably inside SYN
  What happens when middleboxes drop TCP options in data segments

## Slide 71: Multipath TCP using TLV
Advantages
  Multipath TCP could start as regular TCP and move to Multipath only when needed
  Could be implemented as a library in userspace
  TLVs can be easily extended
Drawbacks
  TCP segments contain TLVs including the data and not only the data
    problem for middleboxes, DPI, ..
  Middleboxes become more difficult
Michael Scharf, Thomas-Rolf Banniza , MCTCP: A Multipath Transport Shim Layer, GLOBECOM 2011

## Slide 72: Multipath TCP options
TCP option format
Initial design
  One option kind for each purpose (e.g. Data Sequence number)
Final design
  A single variable-length Multipath TCP option
Kind
Length
Option-specific data

## Slide 73: Multipath TCP option
A single option type
  to minimise the risk of having one option accepted by middleboxes in SYN segments and rejected in segments carrying data
Subtype
Kind Length
Subtype specific data
(variable length)

## Slide 74: TCP options
© O. Bonaventure, 2011
Known option (TS) in Data segments
XD6BHM
Honda, Michio, et al. "Is it still possible to extend TCP?." Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 75: TCP options
© O. Bonaventure, 2011
Unknown option in Data segments
XD6BHM
Honda, Michio, et al. "Is it still possible to extend TCP?." Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 76: Data sequence numbers and TCP segments
How to transport Data sequence numbers ?
  Same solution as for TCP
    Data sequence number in TCP option is the Data sequence number of the first byte of the segment
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Payload
Datasequence number

## Slide 77: Multipath TCP Data transfer
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=2, seq=124,"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457

## Slide 78: TCP sequence number and middleboxes
© O. Bonaventure, 2011
Honda, Michio, et al. "Is it still possible to extend TCP?." Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 79: Which middleboxes change TCP sequence numbers ?
Some firewalls change TCP sequence numbers in SYN segments to ensure randomness
  fix for old windows95 bug
Transparent proxies terminate TCP connections

## Slide 80: Other types of middlebox interference
Data segments
Data,seq=12,"ab"
Data,seq=14,"cd"
Data,seq=12,"abcd"

## Slide 81: Segment coalescing
© O. Bonaventure, 2011
Honda, Michio, et al. "Is it still possible to extend TCP?." Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 82: Data sequence numbers and middleboxes
seq=123,Dseq=0, "a"
seq=456, DSeq=1, "b"
seq=124, DSeq=2,"c"
seq=123, DSeq=2, "ac"
copies one option in coalesced segment
buffers small segments
seq=123, DSeq=0, "ac"

## Slide 83: Data sequence numbers and middleboxes
seq=123,Dseq=0, "ab"
DSeq=0, seq=123,"a"
DSeq=0, seq=124,"b"
Middlebox only understands regular TCP

## Slide 84: Data sequence numbers and middleboxes
How to avoid desynchronisation between the bytestream and data sequence numbers ?
Solution
  Multipath TCP option carries mapping between Data sequence numbers and subflow sequence numbers
    mapping covers a part of the bytestream (length)

## Slide 85: Multipath TCP Data transfer
seq=123,DSS[0->123,len=1],"a"
seq=456, DSS[1->456,len=1],"b"
seq=124, DSS[2->124,len=1],"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457

## Slide 86: Data sequence numbers and middleboxes
seq=123,DSS[0->123,len=1], "a"
seq=456, DSS[1->456, len=1], "b"
seq=124, DSS[2->124, len=1],"c"
seq=123,
DSS[0->123, len=1],
"ac"
DAck=2,ack=124
DSeq=0,ack=457
seq=124, DSS[2->124, len=1],"c"

## Slide 87: Data sequence numbers and middleboxes
seq=123,DSS[0->123,len=1], "a"
seq=456, DSS[1->456, len=1], "b"
seq=124, DSS[2->124, len=1],"c"
seq=123,
DSS[2->124, len=1],
"ac"
DAck=0,ack=125
seq=125, DSS[0->125, len=1],"a"
DAck=3,ack=126

## Slide 88: Multipath TCP and middleboxes
With the DSS mapping, Multipath TCP can cope with middleboxes that
  combine segments
  split segments
Are they the most annoying middleboxes for Multipath TCP ?
  Unfortunately not

## Slide 89: The worst middlebox
Is this an academic exercise or reality ?
seq=123,
DSS[1->123, len=2],
"aXXXb"
DAck=3,ack=125
seq=125,
DSS[3->125, len=2],
"cd"
seq=123,
DSS[1->123,len=2], "ab"
DAck=3,ack=128
seq=128,
DSS[3->125, len=2],
"cd"

## Slide 90: The worst middlebox
Is unfortunately very old...
  Any ALG for a NAT
220 ProFTPD 1.3.3d Server (BELNET FTPD Server) [193.190.67.15]
ftp_login: user `<null>' pass `<null>' host `ftp.belnet.be'
Name (ftp.belnet.be:obo): anonymous
---> USER anonymous
331 Anonymous login ok, send your complete email address as your password
Password:
---> PASS XXXX
---> PORT 192,168,0,7,195,120
200 PORT command successful
---> LIST
150 Opening ASCII mode data connection for file list
lrw-r--r-- 1 ftp ftp 6 Jun 1 2011 pub -> mirror
226 Transfer complete

## Slide 91: Coping with the worst middlebox
What should Multipath TCP do in the presence of such a worst middlebox ?
  Do nothing and ignore the middlebox
    but then the bytestream and the application would be broken and this problem will be difficult to debug by network administrators
  Detect the presence of the middlebox
    and fallback to regular TCP (i.e. use a single path and nothing fancy)

## Slide 92: Detecting the worst middlebox ?
How can Multipath TCP detect a middlebox that modifies the bytestream and inserts/removes bytes ?
  Various options were explored
  In the end, Multipath TCP chose to include its own checksum to detect insertion/deletion of bytes

## Slide 93: The worst middlebox
seq=123,
DSS[1->123, len=2,Inv],
"aXXXb"
seq=123,
DSS[1->123,len=2,V], "ab"
RST, last DSeq=0
RST, last DSeq=0
seq=456, DSS[1->456, len=2,V], "ab"
DAck=3,ack=458

## Slide 94: Multipath TCP Data sequence numbers
What should be the length of the data sequence numbers ?
  32 bits
    compact and compatible with TCP
    wrap around problem at highspeed requires PAWS
  64 bits
    wrap around is not an issue for most transfers today
    takes more space inside each segment

## Slide 95: Multipath TCP Data sequence numbers
Data sequence numbers and Data acknowledgements
  Maintained as 64 bits field
  Implementations can, as an optimisation, only transmit the lower 32 bits of the data sequence and acknowledgements

## Slide 96: Data Sequence Signal option
Cumulative Data ack
A = Data ACK present
a = Data ACK is 8 octets
M = mapping present
m = DSN is 8
Length of mapping, can extend beyond this segment
Computed over data covered by entire mapping + pseudo header

## Slide 97: Cost of the DSN checksum
C. Raiciu, et al. “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.

## Slide 98: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 99: TCP congestion control
© O. Bonaventure, 2008
CNP3/2010.3.
A linear rate adaption algorithm
To be fair and efficient, a linear algorithm must use additive increase and multiplicative decrease (AIMD)
# Additive Increase Multiplicative Decrease
if congestion :
rate=rate*betaC # multiplicative decrease, betaC<1
else
rate=rate+alphaN # additive increase, v0>0

## Slide 100: AIMD in TCP
Congestion control mechanism
  Each host maintains a congestion window (cwnd)
  No congestion
    Congestion avoidance (additive increase)
      increase cwnd by one segment every round-trip-time
  Congestion
    TCP detects congestion by detecting losses
    Mild congestion (fast retransmit – multiplicative decrease)
      cwnd=cwnd/2 and restart congestion avoidance
    Severe congestion (timeout)
      cwnd=1, set slow-start-threshold and restart slow-start

## Slide 101: Evolution of the congestion window
Cwnd
Fast retransmit
Threshold
Threshold
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd
Fast retransmit
Time

## Slide 102: Congestion control for Multipath TCP
Simple approach
  independant congestion windows
Threshold
Threshold
Threshold

## Slide 103: Independant congestion windows
Problem
12Mbps

## Slide 104: Coupling the congestion windows
Principle
  The TCP subflows are not independant and their congestion windows must be coupled
EWTCP
  For each ACK on path r, cwinr=cwinr+a/cwinr (in segments)
  For each loss on path r, cwinr=cwinr/2
  Each subflow gets window size proportional to a2
  Same throughput as TCP if
M. Honda, Y. Nishida, L. Eggert, P. Sarolahti, and H. Tokuda. Multipath Congestion Control for Shared Bottleneck. In Proc. PFLDNeT workshop, May 2009.

## Slide 105: Can we split traffic equally among all subflows ?
12Mbps
12Mbps
12Mbps
D. Wischik, C. Raiciu, A. Greenhalgh, and M. Handley, “Design, implementation and evaluation of congestion control for multipath TCP,” NSDI'11: Proceedings of the 8th USENIX conference on Networked systems design and implementation, 2011.
In this scenario, EWTCP would get 3.5 Mbps on the two hops path and 5 Mbps on the one hop path, less than the optimum of 12 Mbps for each Multipath TCP connection

## Slide 106: Linked increases congestion control
Algorithm
  For each loss on path r, cwinr=cwinr/2
  Additive increase
D. Wischik, C. Raiciu, A. Greenhalgh, and M. Handley, “Design, implementation and evaluation of congestion control for multipath TCP,” NSDI'11: Proceedings of the 8th USENIX conference on Networked systems design and implementation, 2011.

## Slide 107: Other Multipath-aware congestion control schemes
Y. Cao, X. Mingwei, and X. Fu, “Delay-based Congestion Control for Multipath TCP,” ICNP2012, 2012.
T. A. Le, C. S. Hong, and E.-N. Huh, “Coordinated TCP Westwood congestion control for multiple paths over wireless networks,” ICOIN '12: Proceedings of the The International Conference on Information Network 2012, 2012, pp. 92–96.
T. A. Le, H. Rim, and C. S. Hong, “A Multipath Cubic TCP Congestion Control with Multipath Fast Recovery over High Bandwidth-Delay Product Networks,” IEICE Transactions, 2012.
R. Khalili, N. Gast, M. Popovic, U. Upadhyay, J.-Y. Le Boudec , MPTCP is not Pareto-optimal: Performance issues and a possible solution, Proc. ACM Conext 2012
T. Dreibholz, M. Becke, J. Pulinthanath, and E. P. Rathgeb, “Applying TCP-Friendly Congestion Control to Concurrent Multipath Transfer,” Advanced Information Networking and Applications (AINA), 2010 24th IEEE International Conference on, 2010, pp. 312–319.

## Slide 108: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 109: The Multipath TCP control plane
Connection establishment in details
Closing a Multipath TCP connection
Address dynamics

## Slide 110: Security threats
Three main security threats were considered
  flooding attack
  man-in-the middle attack
  hijacking attach
J. Diez, M. Bagnulo, F. Valera, and I. Vidal, “Security for multipath TCP: a constructive approach,” International Journal of Internet Protocol Technology, vol. 6, 2011.
Security goal : Multipath TCP should not be worse than regular TCP

## Slide 111: Hijacking attack

## Slide 112: Multipath TCP Connection establishment
Principle
SYN+ACK, MP_CAPABLE
ACK, MP_CAPABLE
seq=123, DSeq=1, "abc"
SYN, MP_CAPABLE

## Slide 113: Roles of the initial TCP handshake
Check willingness to open TCP connection
  Propose initial sequence number
  Negotiate Maximum Segment Size
TCP options
  negotiate Timestamps, SACK, Window scale
Multipath TCP
  check that server supports Multipath TCP
  propose Token in each direction
  propose initial Data sequence number in each direction
  Exchange keys to authenticate subflows

## Slide 114: How to extend TCP ? Theory
TCP options were invented for this purpose
  Exemple SACK
SYN+SACK Permitted
SYN+ACK SACK Permitted
SACK ?
SACK yes
SACK enabled

## Slide 115: How to extend TCP ? practice
What happens when there are middleboxes on the path ?
SYN+SACK Permitted
SYN
SYN+ACK
SYN+ACK
SACK
no
SACK
no

## Slide 116: TCP options
© O. Bonaventure, 2011
In SYN segments
XD6BHM
Honda, Michio, et al. "Is it still possible to extend TCP?." Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 117: How to extend TCP ? The worst case
What happens when there are middleboxes on the path ?
SYN+SACK Permitted
SYN+SACK Permitted
SYN+ACK
SACK
no
SACK
SYN+ACK SACK Permitted
enabled
Client and server do not agree on TCP extension !!!

## Slide 118: Multipath TCP handshake Does server support Multipath TCP ?
SYN+ACK, MP_CAPABLE[...]
ACK+MPTCPOption
SYN, MP_CAPABLE[...]
Why an option in third ACK ?

## Slide 119: Multipath TCP option in third ACK
SYN+ACK, MP_CAPABLE[...]
ACK
SYN, MP_CAPABLE[...]
No option, disable
Multipath TCP
SYN+ACK

## Slide 120: Multipath TCP handshake Token exchange
SYN+ACK, MP_CAPABLE[ServerToken=5678]
ACK, MP_CAPABLE[ClientToken=1234]
SYN, MP_CAPABLE[ClientToken=1234]
Useful if server wants to send SYN+ACK without keeping any state

## Slide 121: Initial Data Sequence number
Why do we need an initial Data Sequence number ?
  Setting IDSN to a random value improves security
  Hosts must know IDSN to avoid losing data in some special cases

## Slide 122: Initial Data Sequence number
SYN+ACK, MP_CAPABLE
ACK
SYN, MP_CAPABLE
seq=123,
DSS[456->123,len=2],"ab"
seq=789, DSS[458->789, len=2], "cd"
SYN+ACK...
SYN...
First Data or not ?
ACK
Notes: attaquant pourrait injecter le numéro de séquence initial et le choisir

## Slide 123: Initial Data Sequence number
How to fix the IDSN ?
SYN+ACK, MP_CAPABLE[DSeq=67890]
ACK
SYN, MP_CAPABLE[DSeq=23456]

## Slide 124: How to secure Multipath TCP
Main goal
  Authenticate the establishment of subflows
Principles
  Each host announces a key during initial handshake
    keys are exchanged in clear
  When establishing a subflow, use HMAC + key to authenticate subflow

## Slide 125: Key exchange
SYN+ACK, [MyKey="keyDEF"]
ACK[MyKey="keyABC", YourKey="keyDEF"]
SYN, [MyKey="keyABC"]
SYN,[NonceA=123]
SYN+ACK[NonceB=456, HMAC(123,"keyDEF")]
ACK,[HMAC(456,"keyABC")]
MyKey="keyABC"
YourKey="keyDEF"
MyKey="keyDEF"
YourKey="keyABC"

## Slide 126: Putting everything inside the SYN
How can we place inside the SYN segment
  Initial Data Sequence Number (64 bits)
  Token (32 bits)
  Authentication Key (the longer the better)

## Slide 127: Constraint on TCP options
Total length of TCP header : max 64 bytes
  max 44 bytes for TCP options
  size must be multiple of 4 bytes
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options

## Slide 128: TCP options in the wild
MSS option [4 bytes]
  Used only inside SYN segments
Timestamp option [10 bytes]
  Used in potentially all segments
Window scale option [3 bytes]
  Used only inside SYN segments
SACK permitted option [2 bytes]
  Used only inside SYN segments
Selective Acknowledgements [N bytes]
  Used in data segments
http://www.iana.org/assignments/tcp-parameters/tcp-parameters.xml
Only 20 bytes left inside SYN !

## Slide 129: The MP_CAPABLE option
A: DSN Checksum
required or not
B: Extension
crypto
Used inside SYN
Only in third ACK

## Slide 130: Initial Data Sequence Numbers and Tokens
Where is the initial Data Sequence Number
Where is the token ?
TokenA=Upper32(SHA-1(KeyA))
TokenB=Upper32(SHA-1(KeyB))
IDSNA=Lower64(SHA-1(KeyA))
IDSNB=Lower64(SHA-1(KeyB))
There is a small risk of collision,
different keys
same token

## Slide 131: Cost of the Multipath TCP handshake
C. Raiciu, et al. “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.

## Slide 132: The Multipath TCP control plane
Connection establishment in details
Closing a Multipath TCP connection
Address dynamics

## Slide 133: Closing a Multipath TCP connection
RST
RST
How to close a Multipath TCP connection ?
  By closing all subflows ?

## Slide 134: Closing a Multipath TCP connection
seq=123, DSS[1->123 ...], "ab"
DAck=9,ack=128
seq=456, DSS[3->456], "cd"
DAck=5,ack=458
seq=125, DSS[5->125,DATA_FIN ...], "end"
seq=128, FIN
ack=129

## Slide 135: Closing a Multipath TCP connection
FAST Close
SYN+ACK, [...]
ACK[...]
SYN,[...]
SYN+ACK[...]
ACK[..]
SYN, [...]
ACK+FAST_CLOSE
RST
RST

## Slide 136: The Multipath TCP control plane
Connection establishment in details
Closing a Multipath TCP connection
Address dynamics

## Slide 137: Multipath TCP Address dynamics
How to learn the addresses of a host ?
How to deal with address changes
IP=1.2.3.4
IP=4.5.6.7
IP=2.3.4.5
IP=3.4.5.6
IP6=2a00:1450:400c:c05::69

## Slide 138: Address dynamics
Basic solution : multihomed server
IP=2.3.4.5
IP=3.4.5.6
IP6=2a00:1450:400c:c05::69
SYN+ACK, [...]
ACK[...]
SYN, [...]
ADD_ADDR[3.4.5.6]
ADD_ADDR[2a00:1450:400c:c05::69]
SYN,[...]
SYN+ACK[...]
ACK[..]

## Slide 139: Address dynamics
Basic solution : mobile client
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=4.5.6.7
ADD_ADDR [4.5.6.7]
SYN,[...]
SYN+ACK[...]
ACK[..]
REMOVE_ADDR[1.2.3.4]

## Slide 140: Address dynamics in today's Internet
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=10.0.02
ADD_ADDR [10.0.0.2]
SYN [...]
ADD_ADDR [10.0.0.2]
?

## Slide 141: Address dynamics with NATs
Solution
  Each address has one identifier
    Subflow is established between id=0 addresses
  Each host maintains a list of <address,id> pairs of the addresses associated to an MPTCP endpoint
  MPTCP options refer to the address identifier
    ADD_ADDR contains <address,id>
    REMOVE_ADDR contains <id>

## Slide 142: Address dynamics
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=4.5.6.7
ADD_ADDR [4.5.6.7,id=1]
SYN,[id=1...]
SYN+ACK[...]
ACK[..]
REMOVE_ADDR[id=0]

## Slide 143: Agenda
The motivations for Multipath TCP
The changing Internet
The Multipath TCP Protocol
Multipath TCP use cases
  Datacenters
  Smartphones

## Slide 144: Datacenters evolve
Traditional Topologies are tree-based
  Poor performance
  Not fault tolerant
Shift towards multipath topologies: FatTree, BCube, VL2,
Cisco, EC2
…
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.

## Slide 145: Fat Tree Topology [Fares et al., 2008; Clos, 1953]
K=4
1Gbps
1Gbps
Aggregation Switches
K Pods with
K Switches
each
Racks of
servers
Notes: Show multiple paths between servers
Say that network is rearrangeably non blocking
Clos
145

## Slide 146: Fat Tree Topology [Fares et al., 2008; Clos, 1953]
K=4
Aggregation Switches
K Pods with
K Switches
each
Racks of
servers
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.
Notes: Show multiple paths between servers
Say that network is rearrangeably non blocking
Clos
146

## Slide 147: Collisions
Notes: Show multiple paths between servers
Say that network is rearrangeably non blocking
Clos
147

## Slide 148: TCP in data centers

## Slide 149: TCP in FAT tree networks Cost of collissions
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.

## Slide 150: How to get rid of these collisions ?
Consider TCP performance as an optimisation problem

## Slide 151: The Multipath TCP way
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.
Two subflows differ by their source port
ECMP balances the subflows over different paths

## Slide 152: MPTCP better utilizes the FatTree network
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.
Notes: Fairness matters for apps!

## Slide 153: How many subflows does Multipath TCP need ?
Total Throughput
TCP
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.

## Slide 154: Can we improve Multipath TCP ?
Two subflows may follow similar paths

## Slide 155: Improving ECMP
ECMP's hash
  good load balancing
  impossible to predict result
CFLB
  replaces hash with block cipher
  hosts can select paths for Multipath TCP subflows provided they know datacenter topology
G. Detal, Ch. Paasch, S. van der Linden, P. Mérindol, G. Avoine, O. Bonaventure, Revisiting Flow-Based Load Balancing: Stateless Path Selection in Data Center Networks, to appear in Computer Networks

## Slide 156: Multipath TCP with CFLB in Fat-Tree
G. Detal, Ch. Paasch, S. van der Linden, P. Mérindol, G. Avoine, O. Bonaventure, Revisiting Flow-Based Load Balancing: Stateless Path Selection in Data Center Networks, to appear in Computer Networks

## Slide 157: Multipath TCP on EC2
Amazon EC2: infrastructure as a service
  We can borrow virtual machines by the hour
  These run in Amazon data centers worldwide
  We can boot our own kernel
A few availability zones have multipath topologies
  2-8 paths available between hosts not on the same machine or in the same rack
  Available via ECMP

## Slide 158: Amazon EC2 Experiment
40 medium CPU instances running MPTCP
During 12 hours, we sequentially ran all-to-all iperf cycling through:
  TCP
  MPTCP (2 and 4 subflows)

## Slide 159: MPTCP improves performance on EC2
Same
Rack
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.

## Slide 160: Agenda
The motivations for Multipath TCP
The changing Internet
The Multipath TCP Protocol
Multipath TCP use cases
  Datacenters
  Smartphones

## Slide 161: Motivation
One device, many IP-enabled interfaces

## Slide 162
MPTCP over WiFi/3G
8Mbps, 20ms
2Mbps, 150ms

## Slide 163
TCP over WiFi/3G
C. Raiciu, et al. “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.

## Slide 164
MPTCP over WiFi/3G
C. Raiciu, et al. “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.

## Slide 165
MPTCP over WiFi/3G
Multipath TCP
increases
throughput

## Slide 166
MPTCP over WiFi/3G
What happened here?

## Slide 167: Understanding the performance issue
8Mbps, 20ms
2Mbps, 150ms
Window
B
A
C
D
Window full !
No new data can be sent on WiFi path
A
Reinject segment on fast path
Halve congestion window on slow subflow

## Slide 168
MPTCP over WiFi/3G

## Slide 169: Usage of 3G and WiFI
How should Multipath TCP use 3G and WiFi ?
  Full mode
    Both wireless networks are used at the same time
  Backup mode
    Prefer WiFi when available, open subflows on 3G and use them as backup
  Single path mode
    Only one path is used at a time, WiFi preferred over 3G

## Slide 170: Multipath TCP : Full mode
SYN+ACK...
ACK...
SYN...
SYN...
SYN+ACK,...
ACK ...
WiFi
3G/LTE

## Slide 171: Multipath TCP : Backup mode
SYN+ACK...
ACK...
SYN...
SYN,MP_JOIN[Backup...]
SYN+ACK,...
ACK ...
WiFi
3G/LTE
MP_PRIO[B]
Dynamically change backup status of flow

## Slide 172: Multipath TCP : Backup mode
What happens when link fails ?
SYN+ACK...
ACK...
SYN...
SYN,MP_JOIN[Backup...]
SYN+ACK,...
ACK ...
WiFi
3G/LTE
REM_ADDR[id=0]

## Slide 173: Multipath TCP : single-path mode
Multipath TCP supports break before make
SYN+ACK...
ACK...
SYN...
SYN,MP_JOIN
SYN+ACK,...
ACK ...
WiFi
3G/LTE
REM_ADDR[id=0]

## Slide 174: Evaluation scenario
3G: Mobistar
(~2 Mbps, ~80ms)
WiFi:
Belgacom ADSL2+
(~8 Mbps, ~30 ms)

## Slide 175: Recovery after failure
C. Paasch, et al. , “Exploring mobile/WiFi handover with multipath TCP,” presented at the CellNet '12: Proceedings of the 2012 ACM SIGCOMM workshop on Cellular networks: operations, challenges, and future design, 2012.

## Slide 176: Recovery after failure
C. Paasch, et al. , “Exploring mobile/WiFi handover with multipath TCP,” presented at the CellNet '12: Proceedings of the 2012 ACM SIGCOMM workshop on Cellular networks: operations, challenges, and future design, 2012.

## Slide 177: Recovery after failure
C. Paasch, et al. , “Exploring mobile/WiFi handover with multipath TCP,” presented at the CellNet '12: Proceedings of the 2012 ACM SIGCOMM workshop on Cellular networks: operations, challenges, and future design, 2012.

## Slide 178: Conclusion
Multipath TCP is becoming a reality
  Due to the middleboxes, the protocol is more complex than initially expected
  RFC will appear and there is running code !
  Multipath TCP works over today's Internet !
What's next ?
  More use cases
    IPv4/IPv6, anycast, load balancing, deployment
  Measurements and improvements to the protocol
    Time to revisit 20+ years of heuristics added to TCP

## Slide 179: References
The Multipath TCP protocol
  http://www.multipath-tcp.org
  http://tools.ietf.org/wg/mptcp/
A. Ford, C. Raiciu, M. Handley, S. Barre, and J. Iyengar, “Architectural guidelines for multipath TCP development", RFC6182 2011.
C. Raiciu, C. Paasch, S. Barre, A. Ford, M. Honda, F. Duchene, O. Bonaventure, and M. Handley, “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.
A. Ford, C. Raiciu, M. J. Handley, and O. Bonaventure, “TCP Extensions for Multipath Operation with Multiple Addresses,” Internet draft, draft-ietf-mptcp-multiaddressed-12, 2012

## Slide 180: Implementations
Linux
  http://www.multipath-tcp.org
FreeBSD
  http://caia.swin.edu.au/urp/newtcp/mptcp/
Simulators
  http://nrg.cs.ucl.ac.uk/mptcp/implementation.html
  http://code.google.com/p/mptcp-ns3/
S. Barre, C. Paasch, and O. Bonaventure, “Multipath tcp: From theory to practice,” NETWORKING 2011, 2011.
Sébastien Barré. Implementation and assessment of Modern Host-based Multipath Solutions. PhD thesis. UCL, 2011

## Slide 181: Middleboxes
M. Honda, Y. Nishida, C. Raiciu, A. Greenhalgh, M. Handley, and H. Tokuda, “Is it still possible to extend TCP?,” IMC '11: Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference, 2011.
J. Sherry, S. Hasan, C. Scott, A. Krishnamurthy, S. Ratnasamy, and V. Sekar, “Making middleboxes someone else's problem: network processing as a cloud service,” SIGCOMM '12: Proceedings of the ACM SIGCOMM 2012 conference on Applications, technologies, architectures, and protocols for computer communication, 2012.
V. Sekar, N. Egi, S. Ratnasamy, M. K. Reiter, and G. Shi, “Design and implementation of a consolidated middlebox architecture,” USENIX NSDI, 2012.

## Slide 182: Multipath congestion control
  Background
  Coupled congestion control
D. Wischik, C. Raiciu, A. Greenhalgh, and M. Handley, “Design, implementation and evaluation of congestion control for multipath TCP,” NSDI'11: Proceedings of the 8th USENIX conference on Networked systems design and implementation, 2011.
C. Raiciu, M. J. Handley, and D. Wischik, “Coupled Congestion Control for Multipath Transport Protocols,” RFC, vol. 6356, Oct. 2011.
D. Wischik, M. Handley, and M. B. Braun, “The resource pooling principle,” ACM SIGCOMM Computer …, vol. 38, no. 5, 2008.
P. Key, L. Massoulie, and P. D. Towsley, “Path Selection and Multipath Congestion Control,” INFOCOM 2007. 2007, pp. 143–151.
F. Kelly and T. Voice. Stability of end-to-end algorithms for joint routing and rate control. ACM SIGCOMM CCR, 35, 2005.

## Slide 183: Multipath congestion control
  More
Y. Cao, X. Mingwei, and X. Fu, “Delay-based Congestion Control for Multipath TCP,” ICNP2012, 2012.
T. A. Le, C. S. Hong, and E.-N. Huh, “Coordinated TCP Westwood congestion control for multiple paths over wireless networks,” ICOIN '12: Proceedings of the The International Conference on Information Network 2012, 2012, pp. 92–96.
T. A. Le, H. Rim, and C. S. Hong, “A Multipath Cubic TCP Congestion Control with Multipath Fast Recovery over High Bandwidth-Delay Product Networks,” IEICE Transactions, 2012.
R. Khalili, N. Gast, M. Popovic, U. Upadhyay, J.-Y. Le Boudec , MPTCP is not Pareto-optimal: Performance issues and a possible solution, Proc. ACM Conext 2012
T. Dreibholz, M. Becke, J. Pulinthanath, and E. P. Rathgeb, “Applying TCP-Friendly Congestion Control to Concurrent Multipath Transfer,” Advanced Information Networking and Applications (AINA), 2010 24th IEEE International Conference on, 2010, pp. 312–319.

## Slide 184: Use cases
  Datacenter
  Mobile
C. Paasch, G. Detal, F. Duchene, C. Raiciu, and O. Bonaventure, “Exploring mobile/WiFi handover with multipath TCP,” CellNet '12: Proceedings of the 2012 ACM SIGCOMM workshop on Cellular networks: operations, challenges, and future design, 2012.
C. Raiciu, S. Barre, C. Pluntke, A. Greenhalgh, D. Wischik, and M. J. Handley, “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.
C. Pluntke, L. Eggert, and N. Kiukkonen, “Saving mobile device energy with multipath TCP,” MobiArch '11: Proceedings of the sixth international workshop on MobiArch, 2011.
G. Detal, Ch. Paasch, S. van der Linden, P. Mérindol, G. Avoine, O. Bonaventure, Revisiting Flow-Based Load Balancing: Stateless Path Selection in Data Center Networks, to appear in Computer Networks